## Slide 1
OFC 2024 SHOW FLOOR PROGRAMS
Mobile Optics (MOPA) for the 6G Era
Advances in Coherent Lite for Mobile Networks
Tuesday, 26 March, 11:00 – 12:00
Speakers:
Fabio Cavaliere, Ericsson, Italy
Gert Sarlet, Coherent, United States
Name, department name, etc.
Acknowledgements:
Marco Di Stefano, Ericsson, Italy

## Slide 2: Coherent Optics in RAN and Relevant MOPA Blueprints
Metro, long-haul and DCI are coherent optics application domains, as reflected by current standards
  IEEE Std. 802.3-2022 100GBASE-ZR DWDM, 80 km
  OIF 400ZR, 80 km
  OpenROADM 100G/200G/400G, 500/600 km
  ITU-T G.698.2 100G, 120 km and 500 km
  CableLabs 100G and 200G, 80 km
Today, use of coherent optics in RAN is rare
  100G needed in 1-2 years, 400G in 3-4 years
  Need for lower cost, lower power consumption and smaller form factor
Coherent optics would be a “natural” way to upgrade capacity and distance of relevant DWDM MOPA blueprints
  40 km distance would cover all practical use cases
MOPA identified this as a standardization gap

## Slide 3: Cost and Power Consumption Trends
Cost and power consumption of coherent optics are both decreasing: will it be sufficient for RANs?
Indirect cost and energy efficiency benefits will come from the longer transmission distance, enabling network centralization and virtualization.
Significant technological innovation (e.g., a “lighter” DSP) is still needed.
Source: Infinera, Five Considerations for Comparing Optical Power Consumption, April 21, 2020

## Slide 4: Bi-Directional DWDM Trunk Links
In IM-DD transceivers, the Rx is broadband, allowing Tx and Rx to operate at different channels
DWDM Mux/De-mux combine upstream and downstream wavelengths on single trunk fiber, allowing bi-directional transmission with standard duplex transceivers
In DCO transceivers, the Rx is narrowband (only receives the channel aligned with the wavelength of the LO laser)
Generally, small form factor DCO transceivers share a single laser for Tx and Rx, forcing Tx and Rx to operate on the same channel
Such DCO transceivers can not directly be applied to above link

## Slide 5: The Bi-Directional DCO Challenge
Tx
Rx
Rx
Tx
λ1
λ1
λ2
λ2
λ1
λ2
Tx
Rx
Rx
Tx
λ1
λ1
λ2
λ2
λ1
λ2
Option 1: two separate tunable lasers for Tx and local oscillator at Rx
Compatible with both single and double fiber links
No performance penalty
Increases cost by 30%-35%, power consumption by ~20% and requires slightly larger form factor
Tx
Rx
Rx
Tx
λ1
λ1
λ1
λ1
1:2 split
1:2 split
Band-split, interleaver or circulator
Tx
Rx
Rx
Tx
λ1
λ1
λ1
λ1
Circulator
(a)
(b)
(c)
(d)
Option 2: shared tunable laser for Tx and local oscillator at Rx, add circulator for Bi-Di
Smaller impact on cost, no increase in power consumption
Performance impaired due to reflections and potential multi-path interference effects

## Slide 6: Measurement Setup

## Slide 7: Optical Reflection Penalties
Sensitivity penalty vs signal to crosstalk ratio (single reflection)
Chart: Optical signal to crosstalk ratio [dB]
| 15.5 | 14 | 12.899999999999999 | 12 | 11.399999999999999
IEEE Std. 802.3 100GBASE-ZR (SC-FEC) | 1.5 | 2 | 2.9 | 4 | 5.4
OpenZR+ MSA ZR100-OFEC-QPSK | 2.5 | 3.5 | 5 | 7.5 | 20
Two operating modes were tested:
  IEEE Std. 802.3-2022 100GBASE-ZR, DP-DQPSK modulation at 28GBd w SC-FEC
  OpenZR+ MSA ZR100-OFEC-QPSK DP-QPSK modulation at 30GBd w O-FEC
Chart plots Rx sensitivity penalty vs optical signal to crosstalk ratio (OSXR) due to reflections of Tx signal
With a constant signal to crosstalk ratio, no significant change in penalty was observed by increasing fiber distance or varying return losses of near and far splitters

## Slide 8: Application to Existing Blueprint
 | Unit | Tx/Rx A | Circ. |  | Mux |  | Fiber |  | De-mux |  | Circ. | Tx/Rx B
Insertion loss | dB |  | 1.2 |  | 5.5 |  | 6.8 |  | 5.5 |  | 1.2 | 
Return loss | dB |  |  |  | 30.0 |  |  |  | 30.0 |  | 30.0 | 
Directivity | dB |  | 45.0 |  |  |  |  |  |  |  |  | 
Signal power A -> B | dBm | -8.0 | → | -9.2 | → | -14.7 | → | -21.5 | → | -27.0 | → | -28.2
 |  | -53.0 | ← |  | ↓ |  |  |  | ↓ |  | ↓ | 
 |  | -40.4 | ← | -39.2 | ← |  |  |  | ↓ |  | ↓ | 
 |  | -65.0 | ← | -63.8 | ← | -58.3 | ← | -51.5 | ← |  | ↓ | 
 |  | -76.0 | ← | -74.8 | ← | -69.3 | ← | -62.5 | ← | -57.0 | ← | 
Total crosstalk power B -> A | dBm | -40.2 |  |  |  |  |  |  |  |  |  | 
Signal power B -> A | dBm | -28.2 | ← | -27.0 | ← | -21.5 | ← | -14.7 | ← | -9.2 | ← | -8.0
Rx signal power close to back-to-back Rx sensitivity, leaving little margin for reflection penalties
Optical signal to crosstalk ratio less than 12 dB, would result in significant sensitivity penalty (> 2 dB)

## Slide 9: Conclusions
Preliminary test results were presented on the use of optical circulators to enable bidirectional transmission with single laser DCO transceivers.
BiDi DCO transceivers with circulator can be considered for use cases similar to existing MOPA blueprints. However, further analysis is required to determine a reasonable trade-off between requirements for various components to avoid excessive penalties due to reflections.
Dual laser DCO transceivers avoid any impairments due to reflections, but come with additional cost and power consumption.

## Slide 10
Copyright © 2023

## Slide 11: Energy Efficiency Benchmark: IM-DD Pluggables for RAN
100G
50G
25G
2018
2023
2025
SFP56
1x50G
SFP112
1x112G
SFP28
1x25G
2.5W 50 pJ/bit
3.0W 60 pJ/bit
2.0W-2.5W 20-25 pJ/bit
3.0W-3.5W 30-35 pJ/bit
2.5W-3.0W 25-30 pJ/bit
1.8W 36 pJ/bit
7.8 Gb/s/cm3
15.6 Gb/s/cm3
3.9 Gb/s/cm3
BW density (bit rate/volume)
1.8W 72 pJ/bit
2.5W 100 pJ/bit
1.5W 60 pJ/bit
Energy efficiency improves but not fast enough: more power consumption in the same volume
The requirements for outdoor and I-temp operation add further challenges
pJ/bit = mW/Gbps
Short reach grey
BiDi – LAN WDM
DWDM