## Slide 1
Implementation considerations for “tight sync”,
caveats and solution paths
WS14 “Mobile optics for 6G and open cloud RAN: new concepts or more of the same?” - ECOC, 22 Sept 2024
François Fredricx, NOKIA Antonio Tartaglia, Ericsson

## Slide 2: Recap: why“tight” synchronization ?
Distribution of sync via network (PTP)
Network-wide sync of all RUs (air interfaces)
  TAE between any 2 RUs => TE between any RU and PRTC
mMIMO across cluster of RUs (fronthaul)
  TAE between any 2 RUs in cluster => TE between any RU and common clock reference
  Different Categories of accuracy
Localisation accuracy
  Very accurate => only for local PtP links
Classification of intermediate nodes (T-BC)
  Max cTE and dTE and total TE per Class A / B / C / (D) node (ITU-T G.8273.2)
RU
CU
DU
Mobile Core
RU
RU
RU
DU
=> TE per RU-DU
=> TE per RU-PRTC
TAE network-wide
TAE RU cluster
T-BCs
T-BCs
T-BCs
T-BCs
T-GM

## Slide 3: Recap: Role of pluggable modules for tight sync
Synchronization distribution via PTP assumes symmetrical latency in both directions. Known asymmetries can be compensated for.
Mobile fronthaul poses highly demanding requirements in terms of end-end synchronization accuracy between T-GM and RUs
Contribution of the pluggables to latency (a)symmetry and hence to cTE can no longer be neglected
MOPA proposals;
  Allow pluggables to be characterized for their typical Tx and Rx latencies so that these can be taken into account by the host Sync Client (see next slide) => How can they be measured, which info to store in module (EEPROM)
  Allow pluggables to be classified in terms of inaccuracies on their Tx and Rx latencies so that their consumption of the end-end cTE budget can be estimated. => Definition of classes, which info to store in module (EEPROM)

## Slide 4: PTP: considering Tx and Rx sides, and host / pluggable at each side
PCS
PMA
MII
AUI
PMA
PMD
MDI
Medium
Reconciliation Sublayer
PCS
PMA
MII
AUI
PMA
PMD
MDI
Medium
Reconciliation Sublayer
Path data delay Tx side
Reference plane in Tx stack
Measurement plane in Tx stack
TimeSync Client
MAC Client
TimeSync Client
MAC Client
Pluggable
Pluggable
pluggable T0 +/- Tx
Host Tx delay
Pluggable R0 +/- Rx
Host Rx delay
Including Tx Path data delay
Including Rx Path data delay
Path data delay Rx side
Measurement plane in Rx stack
Reference plane in Rx stack

## Slide 5: Implementation-specific Sources of inaccuracies
AM added
AM removed
PCS/FEC (m)
PMA (m:n)
MII
PMA (n:n or gearbox n:p)
PMD (p)
Reconciliation Sublayer
Digital Processing, Multi-lane modules
AUI-n
TimeSync Client
MAC Client
Medium
Medium
MDI
Pluggable
MDI
PMD
PMA
AUI-n
PMA
PCS/FEC
MII
gRS
TS
MAC
DTE XS
PMA
MII
Reconciliation Sublayer
PMA
PMD
AUI-n
PCS (GMP)
MDI
Medium
PMA
PHY XS
MII
Pluggable
MII extender
random
TimeSync Client
MAC Client
Medium
MDI
PMD
PMA
AUI-n
PMA
DTE XS
MII
gRS
TS
MAC
PCS
PMA
MII
PHY XS
MII extender
PCS
host FEC PMA
MII
PMA host FEC
PMD
MDI
Medium
Reconciliation Sublayer
AUI
Pluggable
PCS optical FEC
PMA
TimeSync Client
MAC Client
Medium
MDI
PMD
PMA
AUI-n
PMA
PCS/FEC
MII
gRS
TS
MAC
PCS
PMA
Segmented FEC
Unrelated timings
Unrelated timings

## Slide 6: Avoiding inaccuracies
DTE XS
PMA
MII
Reconciliation Sublayer
PMA
PMD
AUI-n
PCS (GMP)
MDI
Medium
PMA
PHY XS
MII
Pluggable
MII extender
TimeSync Client
MAC Client
Medium
MDI
PMD
PMA
AUI-n
PMA
DTE XS
MII
gRS
TS
MAC
PCS
PMA
MII
PHY XS
MII extender
PCS
host FEC PMA
MII
PMA host FEC
PMD
MDI
Medium
Reconciliation Sublayer
AUI
Pluggable
PCS optical FEC
PMA
TimeSync Client
MAC Client
Medium
MDI
PMD
PMA
AUI-n
PMA
PCS/FEC
MII
gRS
TS
MAC
PCS
PMA
Segmented FEC
PCS/FEC (m)
PMA (m:n)
MII
PMA (n:n or gearbox n:p)
PMD (p)
Reconciliation Sublayer
AUI-n
TimeSync Client
MAC Client
Medium
Medium
MDI
Pluggable
MDI
PMD
PMA
AUI-n
PMA
PCS/FEC
MII
gRS
TS
MAC
Digital Processing, Multi-lane modules
Convention to equalize cyclic Tx and Rx mirrored delays
Deskew to equalize lanes using AMs
Proposal to IEEE 802.3dj
Communicate AM location at Tx to Rx by signaling over GMP
Communicate location of AM removal at Tx to Rx by signaling over GMP
Feedback about AM change to gRS
Feedback about AM change to gRS
IEEE 802.3-cx-2023
IEEE 802.3-cx-2023
Same location
Same location

## Slide 7: Summary – recommendations for optical pluggables
Mobile transport puts severe requirements on PTP synchronization
The latency contribution of optical modules must be compensated in the host
The more performant the module, the higher its functionality complexity, leading to sources of latency variations inducing synchronization inaccuracies
Design choices for avoiding inaccuracies:
  Keep registers of internal Rx and Tx latencies (per electrical lane) as proposed by MOPA
  Apply the principles of IEEE 802.3cx-2023 for compensation of cyclic latencies between Tx and Rx sides and for reporting of AM position to RS
  For coherent modules with MII extenders, segmented FEC: apply the GMP-based feedback of AM position from Tx side to Rx side as described in IEEE 802.3dj proposal https://www.ieee802.org/3/dj/public/24_05/sluyski_3dj_01a_2405.pdf
  (non-coherent modules using MII extenders and/or segmented FEC require further study)

## Slide 8
Thank you
François Fredricx
Fixed Networks R&D, Nokia
francois.fredricx@nokia.com