## Slide 1
Optical Rate and Technology Auto-Negotiation for Mobile Fronthaul Links
Ulf Parkholm, Antonio Tartaglia

## Slide 2: Background
DU
DU
DU
X
Hub Site
X
DU
Complex and heterogenous RAN transport environment, CRAN & DRAN
Advances in silicon and optical technology loosely aligns with new generations of Baseband, Transport and Radio Units
“Brownfield” installation is the norm, maintaining interoperability and compatibility with previous generations is key
Automation and zero touch installation & upgrade is highly advantageous
Technology diversity: “2.5Gb/s to 50Gb/s”, 100Gb/s and higher bandwidth in the future

## Slide 3: Background, continued
Circuit switch technology e.i. CPRI, the workhorse of RAN transport, is being phased out and replaced by packet transport.
Predominantly supported over IEEE 802.3 Ethernet
CPRI offers an “auto detect” mechanism, defined by clause 4.5.3.2
CPRI ”auto detect” mechanism is needed, as CPRI offers a wide range of rates (2.5 to 50Gbps), multiple encoding and FEC options
Common Public Radio Interface

## Slide 4: CPRI auto detect
Primary
Linerat1
Linerat2
Linerat3
Secondary
Linerat3
Linerat4
Secondary
Primary
T1
T1’
T1 0.9s to 1.1s
T1’ 3.9s to 4.1s
* Ethernet could be seen as yet another linerate

## Slide 5: CPRI defined Auto Detect limitations
Primary
Host SOC
Serdes
Retimer
Optical module
Not guaranteed to converge with more than four speed / FEC combinations
T1 Timer 0.9 to 1.1 seconds : very challenging to have short enough RX and TX reconfiguration procedure to allow for sufficient RX adaptation and data link to declare “link up”
Doesn't resolve multi lane or “breakout” scenario ( like 100G  4x 25G )
Advanced retimer based on DSP may require extended time for RX adaptation

## Slide 6: IEEE 802.3 Auto Negotiation
Auto-Negotiation for backplane and copper cable assembly
(Clause 73)
The Auto-Negotiation function shall provide the following:
a) Auto-Negotiation transmit
b) Auto-Negotiation receive
c) Auto-Negotiation arbitration
Peer 1
Peer 2
MAC
PCS
PMA
PMD
Medium
AN
Reconciliation sublayer
PHY
MDI

## Slide 7: IEEE 802.3 Auto Negotiation for CR and KR Clause 73
~300 Mbit
T3
T2
 | Parameter | Min | Typ | Max | Units
T1 | Transition position spacing (period) | 3.2 – 0.01% | 3.2 | 3.2+0.01% | ns
T2 | Clock transition to clock transition | 6.2 | 6.4 | 6.6 | ns
T3 | Clock transition to data transition (data =1 ) | 3.0 | 3.2 | 3.4 | ns
T4 | Transitions in an DME page | 51 | - | 100 | -
T5 | DME page width | 338.8 | 339.2 | 339.6 | ns
T6 | DME Manchester violation delimiter width | 12.6 | 12.8 | 13.0 | ns
Clock transitions
First bit on wire
Transition 1 2 3 4 5 6 7
Data - 1 1 0
Encoding  D0 D1 D2
Bit | Technology
A0 | 1000BASE-KX
A1 | 10GBASE-KX4
A2 | 10GBASE-KR
A3 | 40GBASE-KR4
A4 | 40GBASE-CR4
A5 | 100GBASE-CR10
A6 | 100GBASE-KP4
A7 | 100GBASE-KR4
A8 | 100GBASE-CR4
A9 | 25GBASE-KR-S / 25GBASE-CR-S
A10 | 25GBASE-KR – 25GBASE-KR
A11 | 2.5GBASE-KX
A12 | 5GBASE-KR
A13 | 50GBASE-KR / 50GBASE-CR
A14 | 100GBASE-KR2 /100GBASE-CR2
A15 | 200GBASE-KR4 / 200GBASE-CR4
A16-A22 | RESERVED
“Technology ability field”

## Slide 8: AN in legacy RAN designs
Support of auto-negotiation in legacy RAN designs/systems is not known
Assumption is that RAN equipment is predominantly designed with pluggables
“Universal” ports that need to support multiple types of PMD, both CR and Optical…
Auto-negotiation capability, as per 802.3 Clause 73, is mandatory for copper PMDs – for example for 50GBASE-CR (Clause 136)

## Slide 9: Future of OAN
  Optical is different from copper (CR / KR): not all optical variants may interoperate and there may even be potentially “destructive” combinations: optical OAN cannot be “universal” like it is for copper
  IEEE P802.3dj “200Gbps per lane” Task Force has done a lot of work on auto-negotiation and Inter Sublayer Link Training; OAN has not been considered for now
    Inter-Sublayer Link Training (ILT) , “Ready to Send” concept
    Optical Link training (optical segments in ILT)
    Electrical auto-negotiation
    Optical auto-negotiation
More work on OAN is needed
feature parity with CPRI implementations and with copper links
enabling repeatable, consistent system behaviors with optical pluggables exhibiting different individual dynamic behaviors ( for example: DSP retimers vs. analog retimers vs. linear)
enabling repeatable, consistent system behaviours in presence of complex optical solutions running their own state machines (for example: inter-operation of the auto-tuning intelligence in DWDM tunable pluggables and of host algorithms)
Part of the current 802.3dj Draft (D1.5)
Not in the baseline

## Slide 10
Copyright © 2022xxxx

## Slide 11: Background material
IEEE 802.3-2022
Consideration of a Auto Negotiation for Optical link training
Optical auto-negotiation (OAN) baseline
Optical auto-negotiation (OAN) background