## Slide 1
MOPA(I)
Antonio Tartaglia

## Slide 2: Who let the droids out ?

## Slide 3: Mobile access will write the next page of the AI story
… but how ?

## Slide 4: The fundamental things apply, as time goes by
“Plug it again, Sam”

## Slide 5: Easy predictions
5
High temperature operation will remain important
  Moving extra power at high case temperature, whenever possible
Minimal impact on Precision Time Protocol (PTP) accuracy will remain important
  Designing devices with latency determinism in mind
Uncompromised EMI/EMC performance will remain important
Design of RAN systems may have to come to terms with optical transceivers physics
  High bit rate, long distance, low power: pick two…
Faster optics will be needed
  The growth rate goes up and down, but mobile traffic continues to grow

## Slide 6: Flick of the switch/router

## Slide 7: Reasonable prediction: packet switching will help a lot
CO
Cell site #1
Pkt
DU
Pkt
Cell site #N (typ. 4.8)
Pkt
DU
SFP sized optics
May use larger form factors
Backhaul
S1, N3
DU + CU
Pkt
CRAN hub site
Direct fiber
RU
RU
“Passive WDM”
RU
Pkt
Pkt
“Packet+ WDM”
Backhaul
LLS CRAN
RU
Pkt
Pkt
“Packet switched”
RU
Pkt
“Semi-passive WDM”
vDU
Cloud RAN
RU
Pkt
Pkt
“Packet switched”
Pkt
vDU
RU
Pkt
“Passive WDM + Packet”
Pkt

## Slide 8: Ludicrous speed ?

## Slide 9: Not so obvious prediction: the path beyond 100G
“Ludicrous speeds”, the day they will be used in RAN transport is closer than it looks
  Important to define datacom optics with an eye to future reuse in telecom/RAN, MOPA’s here to help
Adapting emerging technologies from scale-out (rack to rack) AI networking for DRAN blueprints
  High capacity, short distance (up to 2km), lower power consumption
  Highly reliable, low latency, sync friendly
  Do we still need to push for SFP-sized optics ?
  Or should we push for SFP-sized copper/LPO, and add switches to host OSFP/QSFP sized optics ?
Adapting emerging technologies from scale-across (DCI) AI networking for CRAN blueprints
  High capacity, long distance (up to 40km) , higher power consumption
  No obvious path to SFP size so far  will need switches
  Performance vs. cost optimization, simplification
    Coherent lite, quasi-coherent ?
….what if Hollow Core Fiber gets deployed ?
  PAM-4 revival for long distance
  Redefinition of “long distance”, that in RAN is latency limited

## Slide 10: Rearchitecting of the MOPA main technical paper (March 2026)
MOPA Papers 26a:
MO: Market Outlook
RBP: Requirements and Blueprints
NT: New Technologies (incl. operational methods)
Technical Papers on tight Synchronization
Parameters for characterized internal latencies
Pluggable classes for latency variations
Implementation considerations
Technical Paper on Coherent Lite
Tests of single laser coherent bidi transmission based on circulators
Remote Performance Monitoring specification
Sending SFF-8472 Transceiver Management info over G.698.4 frame structure
ITU-T SG15 Q13
IEEE 802.3
OIF
SNIA, OIF
d
ITU-T SG15 Q6
 all MOPA technical publications are publicly available here

## Slide 11: Progress made in the last working cycles
Tight Sync: SNIA SFF 8472 has included MOPA’s pluggable latency parameters, First presentation of the topic to OIF CMIS
Optical Auto Negotiation (OAN): Demo given in ECOC 2025. Working towards MOPA specification.
50G DWDM standardization: common contribution of MOPA members to ITU-T SG15/Q6
Power consumption methodology: measurement of 25G DWDM module power, considerations on power consumption dependence on operating case temperature
Coverage of emerging technologies : Hollow Core Fiber , XR optics, Quasi-coherent optics, LPO monitoring continues in the background
Apr 2025 OFC 2025 | Oct 2025 ECOC 2025 | Mar 2026 OFC 2026
3.2
3.3
26a